## Slide 1: C-TIP Evaluation
Results and Lessons Learned
Talking Freight
18 January 2012
Roger Schiller

## Slide 2: Evaluation Methodology
Real Time Traffic Management and Dynamic Route Guidance in Kansas City
  Actual vs. predicted travel time
  Route compliance
  Time savings vs. default route prediction
Intermodal Move Exchange simulations in Kansas City and Chicago
  Potential matched loads equal potential bobtail reduction
  Empty miles eliminated and fuel saved
Drayage optimization tests in KC and Chicago
  Bobtail reductions, fuel savings
Emissions reduction for all of the above
Delphi study to assess theoretical Chicago deployment

## Slide 3: Example of Vantage Performance Monitoring – Dynamic Route Guidance
19 trips recorded on this route during the test, 6 of which were redirected
Drivers followed the redirections 83% of the time
Projected time was within 10% of actual time 67% of the time
The redirections typically occurred 2 minutes after departure
Drivers saved 7 minutes on average by following the redirect
Average variance between projected and actual time was 4 minutes
Average projected time from the point of redirect was 23 minutes

## Slide 4: Overall Results
* Results assume 3-hour delivery window
** IMEX: Intermodal Move Exchange
WDU: Wireless Drayage Updating
RTTM: Real-Time Traffic Monitoring
DRG: Dynamic Route Guidance
 |  |  |  | Test Results |  |  |  | 
Test | Location | Dates of Test | Description of Test | C-TIP Module Deployed** | Actual or Simulated | Productivity Results | Emission Reductions | Fuel Savings
IXT Drayage Optimization | Kansas City, MO | 6/28/2011 8/31/2011 | Deployment of iPhones to optimize drayage moves | IMEX WDU | Actual | 13% Bobtail Reduction | 8% | 121 Gallons
Pride Logistics Drayage Optimization | Chicago, IL | 6/1/2011 9/30/2011 | Deployment of automated dispatching system with Android smart phones to optimize drayage moves | IMEX | Actual | 52% Bobtail Reduction | N/A | 189 Gallons
Dynamic Route Guidance | Kansas City, MO | 12/1/2010 4/30/2011 | Deployment of RTTM/DRG-enabled iPhones | IMEX WDU RTTM DRG | Actual | 21% Travel Time Improvement | 10% | N/A
Real Time Traffic Monitoring | Kansas City, MO | 12/1/2010 4/30/2011 | Deployment of RTTM/DRG-enabled iPhones | IMEX RTTM | Actual | 19% Travel Time Improvement | 6% | N/A
Kansas City IMEX Simulation | Kansas City, MO | 10/1/2010 1/31/2011 | Simulated matching cross-town railroad container moves | IMEX | Simulated | 135 Empty Trips Eliminated (8% reduction) | N/A | 180 Gallons
Chicago IMEX Simulation | Chicago, IL | 1/1/2011 4/30/2011 | Simulated matching cross-town railroad container moves | IMEX | Simulated* | 1,654 Empty Trips Eliminated (17% reduction) | N/A | 6,864 Gallons

## Slide 5: Kansas City Drayage Optimization Test (IXT)
Month | Bobtail Records | Percent Change | Revenue Loads | Percent Change | Telephones Deployed
April | 837 | - | 1,099 | - | 0
May | 865 | 3% | 1,141 | 4% | 0
June | 1,061 | 23% | 1,388 | 22% | 0
July | 999 | -6% | 1,326 | -4% | 4
August | 924 | -8% | 1,346 | 2% | 12
Source: CS analysis of Profit Tools/IXT truck movement data.
Note: All trips greater than 40 miles, outside of the Kansas City metropolitan area, or with no reported miles have been eliminated.

## Slide 6: Chicago Drayage Optimization Test (Pride Logistics)
 | June | July | August | September
Bobtail Miles | 1,967 | 2,136 | 2,196 | 1,061
Total Miles | 20,280 | 23,479 | 24,677 | 22,593
Percent of Miles in Bobtail | 9.7% | 9.1% | 8.9% | 4.7%
Bobtail Trips | 51 | 53 | 58 | 28
Total Trips | 522 | 586 | 635 | 690
Percent of Trips in Bobtail | 9.8% | 9.0% | 9.1% | 4.1%
Total Loads | 522 | 586 | 635 | 690
Drivers | 13 | 15 | 15 | 15
Average Loads per Driver | 40 | 39 | 42 | 46
Source: Pride Logistics, LLC.
Note: June through August is the baseline; September is the test period.

## Slide 7: RTTM and DRG Emissions Reduction
Source: CS analysis of RTTM and DRG move records.

## Slide 8: Delphi Study
Iterative polling of subject matter experts
  Dray trucking, intermodal rail, steamship lines
Asked to evaluate a theoretical Chicago deployment
General agreement that substantial benefits could be achieved
  RTTM and DRG could save up to 10% travel time per trip on average
  Bobtails might be reduced by 15% or more

## Slide 9: Conclusions and Lessons Learned
Successful proof-of-concept
  Technology can address some of the negative impacts of cross-town freight
  Congestion mitigation, emissions reduction, truck travel time savings
Operational constraints limited the Kansas City test
  Railroads had limited participation
  Industry may lack the collaborative mentality needed to make a cooperative dispatch platform work
Future work should leverage recent private sector advances in traveler information
  E.g. smart phone-based dynamic routing